## Slide 1: MD 404 Mobile LIDAR Pilot MDOT - SHA
2018

## Slide 2: Mobile LIDAR System (MLS)
Mobile LiDAR (Light Detection and Ranging): Imaging system that collect geospatial data by measuring the distance to a target by illuminating that target with a laser light. Mobile systems collect up to 1.4 million 3D points of data at highway speed at a range of approximately 100 meters. Images from high definition cameras (resolution up to 3296 x 2472 pixels) that can capture a selectable rate of 100 to 500 frames per mile.

## Slide 3
Project area of Maryland State Highway Route 404, from the interchange with U.S. Highway 50 (near Wye Mills) and terminating at the Highway 404/Business 404 interchange west of Denton (approximately 11.5 miles).
MD 404 widening project

## Slide 4
Mobile LiDAR Mission Plan
Photographs captured in JPG format
Calibrated LIDAR 3D point cloud in LAS and POD formats (can be used in Microstation)
http:// link to Michael Baker’s 3D Streaming Orbit environment for visualization and measurement
ESRI Geodatabase in accordance with approved Data Dictionary
WebViewer training session
Recorded session on LiDAR point cloud integration with MicroStation
Deliverables

## Slide 5
MD 404 - 3D Point Cloud Data Extraction
Barriers
Bridge Decks
Mowable Areas
Curve and Grade
Cross Slope
Lane Information
Shoulder Information
Median Information

## Slide 6
Sign Panels
Sign Installs (posts, etc.)
Lightpoles
Lighting Panels
Lighting Signs
Raised Pavement Markings
Rumble Strips
Painted Lines
MD 404 - 3D Point Cloud Data Extraction

## Slide 15: Orbit Web Viewer
http://maps.poledata.net:443/publications/MD404-Imagery/index.html